## Slide 1
CPEN 315 — FINAL PROJECT
BUILDING
A CPU
From Logic Gates to VHDL
Part A: 16-bit CPU in Logisim Evolution
Part B: 32-bit MIPS Processor in VHDL
University of Ghana • School of Engineering Sciences • 2025/2026

## Slide 2
Project Overview
A two-stage journey from visual circuit design to hardware description language
PART A
16-bit CPU in Logisim
Visual circuit design environment
16-bit ALU: 14 arithmetic + 6 relational ops
Registers, RAM, Control Unit
13 MIPS instruction subset
Full datapath assembled in Logisim
PART B
32-bit MIPS in VHDL
Hardware Description Language (VHDL)
5 core components implemented
GHDL simulation + GTKWave waveforms
8 opcodes, 5 ALU operations
All 5 testbench tasks passed

## Slide 3
PART A
16-bit CPU in Logisim Evolution
Visual circuit design • Arithmetic Logic Unit • Registers • Control Unit • Full Datapath

## Slide 4
PART A
16-bit CPU Architecture
Instruction Set Architecture
R-FORMAT
op(3) | rs(3) | rt(3) | rd(3) | funct(4)
Arithmetic ops
I-FORMAT
op(3) | rs(3) | rt(3) | Immediate
Memory + Branch
J-FORMAT
op(3) | Target Address
Jumps
Supported Instructions (13)
add
R[rd] = R[rs] + R[rt]
sub
R[rd] = R[rs] - R[rt]
and / or
Bitwise operations
slt
Set on Less Than
jr
PC = R[rs]
lw / sw
Load / Store word
beq
Branch if equal
addi / slti
Immediate ops
j / jal
Jump / Jump & Link

## Slide 5
PART A
16-bit Arithmetic Logic Unit
Arithmetic Operations (14)
0
ADD: A + B
1
AND: A & B
2
OR: A | B
3
XOR: A ^ B
4
DIV: A / B
5
MOD: A % B
6
MULT: A × B
7
SUB: A - B
8
SLL A by 2
9
SLL B by 2
10
SRL A by 2
11
SRL B by 2
12
2's comp -A
13
2's comp -B
Relational Operations (6)
0
A > B
1
A == B
2
A >= B
3
A < B
4
A <= B
5
A != B
Port Map
IN
A[15:0]
Input operand A
IN
B[15:0]
Input operand B
IN
AUSel[3:0]
Arithmetic select
IN
RUSel[2:0]
Relational select
OUT
AUResult[15:0]
Arithmetic result
OUT
RUResult[0]
Relational result (1-bit)

## Slide 6
PART A
Control Unit & Full Datapath
Control Unit Signal Table (opcode → control signals)
Instruction
reg_dst
mem_to_reg
alu_op
jump
branch
mem_rd
mem_wr
alu_src
reg_wr
R-type
01
00
10
0
0
0
0
0
1
lw
00
01
00
0
0
1
0
1
1
sw
00
00
00
0
0
0
1
1
0
beq
00
00
01
0
1
0
0
0
0
addi
00
00
11
0
0
0
0
1
1
j
00
00
00
1
0
0
0
0
0
jal
10
10
00
1
0
0
0
0
1
slti
00
00
10
0
0
0
0
1
1
Datapath Components:
16-bit ALU
Register File (8 regs)
Instruction Memory (ROM)
Data Memory (RAM)
Program Counter
Sign Extender
MUXes & Adders

## Slide 7
PART B
32-bit Single-Cycle MIPS Processor in VHDL
GHDL Simulator • GTKWave • VS Code • VHDL-2008 Standard

## Slide 8
PART B
32-bit MIPS Processor Architecture
Instruction Memory
instruction_memory.vhd
16-entry ROM, 32-bit wide. PC selects instruction. Returns NOP if PC ≥ 32.
Register File
register_file.vhd
8 × 32-bit registers. R0 hardwired=0. Async read (2 ports), sync write.
ALU
alu.vhd
ADD, SUB, AND, OR, SLT. Zero flag for BEQ. Purely combinational.
ALU Control
alu_control.vhd
2-level decoder: ALUOp + funct → 3-bit alu_control signal.
Data Memory
data_memory.vhd
256 × 32-bit synchronous RAM. Separate read/write enables.
Control Unit
control_unit.vhd
Decodes 3-bit opcode → 10 control signals for the datapath.

## Slide 9
PART B
Task 1: Data Memory + Task 2: ALU
Task 1 — Data Memory
256 × 32-bit synchronous RAM
Op
Address
Data Written
Data Read
✓
WRITE→READ
2
1,024
1,024
PASS
WRITE→READ
4
429,496
429,496
PASS
RETAIN CHK
2
—
1,024
PASS
GTKWave — tb_data_memory.vcd
clk → toggles every 5 ns (10 ns period)
Write 0x00000400 → addr 2 @ rising edge
Read back 0x00000400 ✓ next cycle
Write 0x000691F8 → addr 4, retain check ✓
Task 2 — ALU Operations
32-bit combinational: ADD, SUB, AND, OR, SLT
Op
A
B
Result
✓
ADD
2,500
25,000
27,500
PASS
SUB
540,250
37,800
502,450
PASS
AND
53,957
30,000
20,512
PASS
OR
746,353
846,465
1,046,897
PASS
SLT
58,847,537
72,464,383
1 (A<B)
PASS
Zero flag: SUB(0xABCD, 0xABCD) → result=0 → zero='1' ✓

## Slide 10
PART B
Task 3: Register File + Task 4: Instruction Memory
Task 3 — Register File
8 × 32-bit • Async reads • Sync write • R0 = 0
Reg
Value Written
Hex
✓
R1
1,934,858
0x001D908A
PASS
R3
8,558,447
0x008282AF
PASS
R5
203,848,544
0x0C283660
PASS
R7
20,670,420
0x013A9794
PASS
R0
N/A (hardwired)
0x00000000
PASS
Dual-port reads: R1+R3 simultaneously → correct
Async: data appears immediately on address change
Wave shows reg_write_en going low after writes
Task 4 — Instruction Memory
Register map: $t0=R1 $t1=R3 $t2=R5 $t3=R7
PC
Instruction
Hex Encoding
0x00
add $t0, $t1, $t2
0x0D420000
0x01
sub $t2, $t2, $t3
0x17440400
0x02
and $t1, $t2, $t0
0x14580800
0x03
or $t2, $t3, $t1
0x1ED41800
0x20
NOP (out of range)
0x00000000
Combinational: no clock needed — instruction changes instantly
PC=0x20 → returns 0x00000000 (boundary protection)
4 instructions decode correctly from 32-bit encoding

## Slide 11
PART B
Task 5: Control Unit — Signal Table
3-bit opcode → 10 datapath control signals
Instruction
Opcode
reg_dst
mem_to_reg
alu_op
jump
branch
mem_rd
mem_wr
alu_src
reg_wr
R-type (add)
000
01
00
10
0
0
0
0
0
1
slti
111
00
00
10
0
0
0
0
1
1
j
101
00
00
00
1
0
0
0
0
0
jal
110
10
10
00
1
0
0
0
0
1
lw
001
00
01
00
0
0
1
0
1
1
sw
010
00
00
00
0
0
0
1
1
0
beq
011
00
00
01
0
1
0
0
0
0
addi
100
00
00
11
0
0
0
0
1
1
jal: only instruction with jump=1 AND reg_write=1 (saves PC+4 to R7)
sw: only instruction with mem_write=1 but reg_write=0 (store doesn't write to register)
beq: only instruction with branch=1 — gates the branch adder with the ALU zero flag

## Slide 12
PART B
GTKWave Simulation Results
tb_alu.vcd
6 transitions @ 20 ns each
alu_control: 000→001→010→011→100→001
Results: 27500, 502450, 20512, 1046897, 1, zero='1'
tb_data_memory.vcd
Sync write then read
0x00000400 @ addr 2
0x000691F8 @ addr 4 → both retained
tb_register_file.vcd
Async dual-port reads
R1,R3,R5,R7 written then read
Simultaneous port reads confirmed
tb_instruction_memory.vcd
Combinational ROM fetch
PC 0→1→2→3: 4 instructions
PC=0x20 → 0x00000000 (NOP) ✓
tb_control_unit.vcd
8 opcode cycles
All 10 signals correct per opcode
jal: jump=1 + reg_write=1 ✓
✓ ALL 5 TESTBENCHES PASSED

## Slide 13
Key Design Decisions
Async Reads, Sync Writes
Register file and instruction memory reads are combinational — data is available within the same clock cycle to feed the ALU. Writes are clocked to prevent races.
R0 Hardwired to Zero
Writes to R0 are blocked by gating on reg_write_dest ≠ '000'. Reads always return 0x00000000. This is the standard MIPS convention enforced in hardware.
Two-Level ALU Decoding
Main Control Unit outputs ALUOp (2-bit). ALU Control refines this with the funct field (3-bit) from R-type instructions to produce the final 3-bit alu_control.
Zero Flag for BEQ
The ALU performs SUB for BEQ instructions. If result = 0x00000000, the zero flag goes high. This single bit gates the branch adder output in the datapath.
Boundary Protection (Instruction Memory)
When PC ≥ 0x20 (32 decimal), instruction memory outputs 0x00000000 (NOP). Prevents fetching garbage beyond the 16-entry ROM.
Single-Cycle Architecture
Every instruction — simple or complex — completes in exactly one clock cycle. Simpler to design and verify than pipelined, at the cost of clock speed.

## Slide 14
Conclusion
14+6
ALU Operations
(Part A)
13
MIPS Instructions
Supported
5
VHDL Components
Implemented
5/5
Testbench Tasks
Passed
Key Learnings
Translated ISA theory into working hardware components in both visual and HDL environments
Understood single-cycle datapath timing: why async reads are mandatory for single-cycle design
Verified hardware behaviour through testbenches and GTKWave waveform analysis
Gained proficiency in VHDL-2008 with GHDL simulation and VS Code workflow
University of Ghana • CPEN 315 Computer Organization & Architecture • 2025/2026 • Prof. R.A. Sowah